Appendix F - The Ionospheric Model
Contents

# Ionospheric Model
Although the ionospheric model used by both Scimitar and Exmore is the same, the two models operate differently. In the off-line system the model provides time interpolation between all of the ionospheric data input values in the ADS (VI traces, OI traces, and geo-location events). In the real-time system (Exmore) time interpolation is not used; the latest ionospheric inputs (VI traced data, OI traced data for the mission, and geo-move data for the mission) are used as soon as they become available. Exmore maintains a separate ionospheric model for each mission.
## Model Assumptions
### Spherical Ionosphere
The model assumes that the ionosphere is a concentric sphere around a spherical earth. It assumes that the virtual height measured over the site is the same as the virtual height downrange. The vertical height is location independent. The model uses a virtual height relative to the surface of the earth, assumed to be sea level. The altitude assumed for the target is sea level. The model also assumes a horizontal virtual height reflection, but does not account for non-tangential reflections.
The assumption that the virtual height measured over the site is the same as the virtual height downrange only applies in the absence of geo-location events. When a track point has been geo-located, the vertical height of the ionosphere becomes a linear function of ground range as described later in this appendix.
### Flat Earth Approximation
The flat Earth approximation only applies to the conversion of the quasi-vertical sounding to a true vertical sounding. The distance between the transmitter and receiver is not large enough to require a curved Earth approximation. However, the curvature of the Earth is significant in the target geolocation equations.
### Spherical Earth
The Earth model used in the equations is a perfect sphere. The same Earth radius, sea level, applies to the site location, the reflection point and the target location.
### Linear and Cubic Spline Interpolation
The model calculates a table of discrete values for each sounding. When interpolating operator entered data (traced VI and OI data) or data where there are only two adjacent points, linear interpolation is used to determine the values between two adjacent values. If enough data points exist and the model is interpolated between calculated data points, cubic spline interpolation is used.
### Ionospheric Model Input Parameters
The model uses the input parameters shown in Table F -1.
Table F‑1. Model Inputs
VI Inputs:
Quasi-Vertical Height
Quasi-Vertical Frequency
Propagation Layer
Time of VI Sounding
OI Inputs:
Oblique Range
Oblique Frequency
Oblique Layer
Time of OI Sounding
Area of Interest of OI Sounding
Measured/Entered Data Inputs:
Target Propagation Layer (Operator Selected)
Azimuth Repetition Interval (Operator Selected)
Target Phase
Target Radar Range (Integrated Velocity)
Target Time
Geo-Location Azimuth Offset
Geo-Location Ground Range Offset
ROP Parameters:
Antenna Mechanical Boresight
Antenna Tilt Angle
Antenna Elevation Angle (Design - Fixed Antennas, Steered Elevation Angle - Flex Antennas)
Antenna Delay Bias
Antenna Steer Angle (Electrical + Flex Steer)
Antenna Baseline Separation
Operating Frequency
Area of Interest of ROP
Site Parameters:
Transmit/Receive Separation
Transmit/Receive Bearing
Receive Site Location (Lat/Long)
General Constants:
Radius of Earth
Speed of Light
Smith Factor

The model determines target position from the input integrated velocity and phase values for each extracted data point. For each extracted point, the model computes the target location (ground range and azimuth) at the two closest sounding times, then performs linear interpolation in time to determine the actual location at the time of the data point.
The model is designed to accept either target radar range or integrated velocity as an input. Scimitar uses the integrated velocity input while Exmore uses the radar range input. The model accepts a single phase value and radar range for each track for each time interval. When multiple modes are present for the same track at the same time, the averaged values from each mode are used to produce a single track phase value and radar range. Radar range and integrated velocity values from the metric data file were calculated using a rounded value for the speed of light. The first calculation performed by the ionospheric model is to convert these values using a more accurate value for the speed of light. The integrated velocity in the Scimitar model is: IV = IVmdf * 2997924.58 / 3000000. The radar range in the Exmore model is: RR = RRmdf * 2997924.58 / 3000000.
In Scimitar, the antenna number and the antenna band for the fixed antenna determine the antenna parameters needed by the model. In Exmore, it is the BFN and the antenna band. The flex antenna requires status indicating the current steer to be used in the model.
As a part of the signature extraction process the operator assigns each track segment to a propagation layer. The assigned layer determines which set of tables the model uses. The model implements each layer independently.
In Scimitar, the model uses one set of tables for each ADS. Thus, an ADS can only correctly handle OI soundings from one AOI. If OI soundings from different AOIs (collected using different BFNs) are mixed within a single ADS, the ionospheric model will interpolate between the OIs in time order, without regard for the fact that they represent different paths through the ionosphere.)
The azimuth repetition interval (ARI) provides the ability to differentiate between cyclical phase values. The model initially assumes that the azimuth will correspond to the primary center lobe of the receive antenna (ARI 0), however the ARI associated with the extracted data overrides the assumption and determines which azimuth repetition interval to use in calculating the target azimuth from the measured phase.
### Ionospheric Model Output Parameters
The calculated output parameters of the ionospheric model are shown in Table F -2. Note that these parameters are calculated for every extracted track point.
Table F‑2. Model Outputs
Receive Elevation Angle (Ray Path)
Receiver Path Length
Receiver Ground Range
Transmit Elevation Angle (Ray Path)
Transmitter Path Length
Transmitter Ground Range
Virtual Height
Target Azimuth
Target Latitude
Target Longitude
Target Ray Receive Angle (Ray Path)
Target Ray Reflect Angle (Ray Path)
Alternate Azimuth (Based on next closest ARI)
Alternate Receiver Ground Range (Based on next closest ARI)
Alternate Latitude (Based on next closest ARI)
Alternate Longitude (Based on next closest ARI)

## Input of Quasi-vertical Frequency and Height Pairs for each Ionospheric Layer
### Scimitar
The primary means of inputting the pairs of quasi-vertical height frequency and heights is by processing the raw VI soundings from tape and tracing the layers, using the Scimitar displays.
A VI data loader is also provided which allows the operator to load a series traced of frequency and quasi-vertical height pairs directly into the system, although as a result of the Phase 2/3 ADP upgrade (Exmore) in 1999 this tool should no longer be necessary except in unusual situations.
### Exmore
The pairs of quasi-vertical height frequency and heights are generated by tracing the VI soundings. The traced VI data is applied to the ionospheric models for all missions.
## Conversion of Vertical Ionogram Pairs from Quasi-vertical Heights to True Vertical Height
The sounding system is bi-static; the transmitter is separated from the receiver. The sounder transmitter is at the transmit site, and the sounder receiver is at the receive site.
The model converts the quasi-vertical frequency and height pairs to true vertical frequency and height pairs because of the difference between the sounders assumed propagation and the actual propagation. (Note: In the actual Scimitar implementation, the Sounding Catalog class (not the Iono Model) performs the conversion of quasi-vertical frequency and height pairs to true vertical frequency and height pairs.)
The sounder assumes that the receiver and the transmitter are co-located, then begins timing the signal when the transmitted wave is first received at the receiver. The propagation delay between the two sites affects the conversion from quasi-vertical to true vertical by changing the actual path length.
The conversion calculates the actual height at which the reflection occurred by determining the path length from the transmitter to the receiver. This path length includes the error because of the separation between transmitter and receiver and the height calculated by the sounding system. The true vertical height is the height of the triangle formed by the transmitter, receiver and reflection point. This relationship is shown in Figure F -1.

Figure F‑1. Quasi-vertical Sounding
The operator enters an arbitrary number of extracted quasi-vertical pairs for each ionospheric layer and the model calculates the vertical height for each input point as shown in the following equations.
(0)
(
0)
where:
VIH	Vertical Height
DTXRX	Distance between Transmitter and Receiver
QVIH	Quasi-vertical height

## Conversion of Quasi-vertical Frequencies to True Vertical Frequencies
### Scimitar
Next, the model converts the quasi-vertical frequencies to account for the angle of incidence into effective vertical frequency. The model determines the vertical frequency by decomposing the quasi-vertical frequencies into a vertical frequency component. The vertical frequency component equals the quasi-vertical frequency multiplied by the cosine of the angle of incidence, as shown in the equations below. (Note: Again, in the actual Scimitar implementation, the Sounding Catalog class (not the Iono Model) performs the conversion of quasi-vertical frequencies to true vertical frequencies.)
### Exmore
Next, the model converts the quasi-vertical frequencies to account for the angle of incidence into effective vertical frequency. The model determines the vertical frequency by decomposing the quasi-vertical frequencies into a vertical frequency component. The vertical frequency component equals the quasi-vertical frequency multiplied by the cosine of the angle of incidence, as shown in the equations below.

(
0)
(
0)
where:
VIH	Vertical Height
VIF	Vertical Frequency
DTXRX	Distance between Transmitter and Receiver
I	Angle of Incidence
QVIF	Quasi-vertical frequency
QVIH	Quasi-vertical height

## Normalization of True Vertical Frequency and Height Pairs
The number of operator entered VI frequency and height pairs and the frequency difference between each pair varies depending on how the operator traces the VI Sounding data. The operator traced points for each layer are normalized so that the number of true vertical frequency and height pairs is predefined and the frequency distance between each pair is constant, as shown in Figure F -2. The number of normalized pairs is a compile-time parameter and is currently set to 20.

Figure F‑2. Normalized Frequency
The results of the normalization are a set of 20 pairs of true vertical frequency and height, at evenly spaced frequency intervals between the first and last frequencies of the original data. The true frequency values of the points are calculated using a linear interpolation between the true frequency calculated for the operator entered (or traced) quasi-vertical frequency. The height values associated with each frequency are generated by using the corresponding normalized vertical frequency to linearly interpolate the true vertical frequency to determine true vertical height.
## Input of Oblique Ionogram Leading Edge Frequency and Range Pairs for each Ionospheric Layer and Area of Interest
The pairs of leading edge frequency and range are entered by the operator tracing the OI soundings for the specific mission.
In Scimitar, an OI data loader is also provided which allows the operator to load a series of traced frequency and quasi-vertical height pairs directly into the system, although as a result of the Phase 2/3 ADP upgrade (Exmore) in 1999 this tool should no longer be necessary except in unusual situations.
## Normalization of Oblique Ionogram Leading Edge Frequency and Range Pairs
As in the case of true vertical frequency and height pairs, the model normalizes the oblique ionogram leading edge frequency and range pairs. The result is a table of oblique ionogram leading edge frequency and range pairs that are equally spaced in frequency. The number of normalized pairs is also a compile time parameter and is currently set to 20.
## Calculation of Synthetic OI Receiver Path Length
The model determines the receiver path length by taking a series of ground ranges (100 km to 5500 km, in 100 km steps) and determining the propagation path required to reach each receiver ground range based on each of the normalized true vertical height values for each VI. (Currently set to 20.)
The example shows the results for a receiver ground range table based on a series of three normalized vertical heights.
Table F‑3
	GRRX #1	GRRX #2	GRRX #3	GRRX #4
VIH #1	PathRX #11	PathRX #12	PathRX #13	PathRX #14
VIH #2	PathRX #21	PathRX #22	PathRX #23	PathRX #24
VIH #3	PathRX #31	PathRX #32	PathRX #33	PathRX #34

Drawn as Flat earth for clarity; actual model uses spherical earth, with concentric spherical ionosphere
Figure F‑3. Multiple Propagation Paths
When a geo-position offset is added to the system, it modifies the ionospheric model so that the vertical height becomes a function of ground range. Figure F -4 shows the effect of repositioning a track point from a ground range of 600 to a new ground range of 650. The vertical height is modified so that it remains at the measured value for the point halfway between the transmit and receive sites, but varies (with a fixed slope) as a function of the target ground range. When there are multiple geo-position events within a single ADS at different times (for the same propagation layer), the model interpolates between them so that the vertical height becomes a function of both time and target ground range. Throughout the rest of this discussion of the ionospheric model, the VIH should be understood to be a function of target ground range if a geo-position offset has been entered for any track; otherwise it remains a constant value regardless of range. Geo-positioning a target also introduces an azimuth offset which is applied to the output of the ionospheric model as described in Section F.15.
### Vertical Height Offsets in Scimitar
Iono Model calculates vertical height offsets to be applied to heights corresponding to all ground range points either by interpolation, for ground points between the overhead measurement and the geomoved midpoint, or extrapolation, for ground points beyond. The offsets are calculated using the formula

Iono Model applies the new VH array to all ionospheric model tables that use vertical height, for instance the transformed path length array and elevation angle array.

Figure F‑4. Effects of Geo-Positioning
The model assumes that the Earth and ionosphere are perfect concentric spheres and that the target and receiver are both at sea level. For each receiver ground range, an arc representing the receiver ground range from the receiver to the target connects the receiver and the target. For each virtual height, the propagation path connects the reflection point, the receiver and target. The reflection point is directly over the midpoint of the ground range, at an altitude equal to the vertical height. Two triangles are used to determine the receiver path length. The vertices of the triangles are the receiver or target, the reflection point and the center of the Earth. The angle between two sides intersecting in the center of the earth is half the receiver ground range divided by the radius of the earth (angle of intersecting arc). By creating a right triangle from the site to the radius plus height side, one can solve for the intermediary value and then use the other right triangle to determine half the receiver path length.

Figure F‑5. Propagation

Figure F‑6. Propagation Triangle
(
0)
(
0)
(
0)
(
0)
(
0)
(
0)
where:
X	1/2 the straight line segment connecting the receiver and the target.
Y	The segment from the reflection point to the intersection with segment X
Y’	The Segment from the center of the Earth to the intersection with segment X
GRRX	Ground Range from Receiver
PathRX	Path Length from Receiver
VIH	Vertical Height (for the applicable ground range)
RE	Radius of Earth (sea level)

## Calculation of Synthetic OI Receiver Elevation Angles
The model calculates a receiver elevation angle for each combination of receiver ground range and VI height. The model determines the receiver elevation from the propagation triangle, Figure F -3. The receiver elevation angle is the angle at the receive antenna vertex minus 90 degrees. The radius of the earth always intersects the sphere at a perpendicular angle, and the receiver elevation angle is the angle of the path above the ground intersection.

Table F‑4
	GRRX #1	GRRX #2	GRRX #3	GRRX #4
VIH #1	Rx Elevation Angle	Rx Elevation Angle	Rx Elevation Angle	Rx Elevation Angle
VIH #2	Rx Elevation Angle	Rx Elevation Angle	Rx Elevation Angle	Rx Elevation Angle
VIH #3	Rx Elevation Angle	Rx Elevation Angle	Rx Elevation Angle	Rx Elevation Angle

(
0)
(
0)
(
0)
where:
PathRX	Path Length from Receiver
RR	Radar Range
VIH	Vertical Height (for the applicable ground range)
RE	Radius of Earth (sea level)
	Angle at the receiver
	Elevation Angle at Receiver less 90 º for the intersection with the Surface of the Earth.

## Calculation OI Oblique Frequencies
The model calculates oblique frequencies from the true vertical frequency and height pairs to determine the effective frequency at the reflection point. Since each height corresponds to a particular vertical frequency, the calculated oblique frequency is the frequency that reflects at the same height. The model calculates oblique frequency for each combination of receiver ground range and virtual height.
Table F‑5. Oblique Frequencies
	GRRX #1	GRRX #2	GRRX #3	GRRX #4
VIH #1	Oblique Freq	Oblique Freq	Oblique Freq	Oblique Freq
VIH #2	Oblique Freq	Oblique Freq	Oblique Freq	Oblique Freq
VIH #3	Oblique Freq	Oblique Freq	Oblique Freq	Oblique Freq

(
0)
(
0)
where:
OIK	Oblique Correction Factor (Only if OI Sounding data exists.)
OIF	Oblique frequency
k	Smith Factor
VIF	Vertical Frequency
I	Angle of Incidence
PathRX	Path Length from Receiver
VIH	Vertical Height (for the applicable ground range)
GRRX	Ground Range from Receiver
RE	Radius of Earth (sea level)

The model then converts the vertical frequency into an oblique frequency. The oblique frequency represents the incoming frequency that has the specified vertical component necessary for a particular vertical height. The oblique frequencies calculated correspond to each normalized VI frequency. Using the frequency and the angle of incidence one can find the actual frequency that would reflect in that particular case. There are two factors modifying the model: the Smith factor and the OI correction factor (OIk).
The Smith factor is a function of ground range (km):
(
0)
where:
k	Smith Factor
GRRX	Ground Range from Receiver

The OI correction factor matches the calculated oblique frequencies to the results from an actual oblique sounding. Oblique frequencies are first calculated from the VI data without the OI correction factor. If oblique sounding data does not exist, then no correction is done. If oblique sounding data does exist, then the OI correction factor is calculated and applied to each calculated oblique frequency. The OI correction factor is a function of ground range and is determined as follows:
1. Find the maximum oblique frequency for a ground range within the oblique frequency table,
2. From the synthetic OI path length table, find the synthetic OI path length corresponding to the maximum oblique frequency (e.g., If the maximum oblique frequency for GRRX #1 is OIF #13, the corresponding OI path length is PathRX #13)
3. Use the synthetic OI path length to interpolate the Normalized OI Leading Edge Frequency/Range table to determine a normalized frequency (NF)
4. Divide the normalized frequency (NF) by the maximum oblique frequency (e.g., OIF #13).
## Interpolation of Receiver Path Length based on Operating Frequency
The model has already calculated the receiver path length for a series of receiver ground ranges corresponding to each virtual height. The actual radar operating frequency narrows the possibilities down to a single value for each parameter for each ground range. Based on the actual operating frequency, the model interpolates the receiver path lengths corresponding to the oblique frequencies in order to calculate the receiver path length for each ground range at the current frequency.
## Interpolation of Receiver Elevation Angle based on Operating Frequency
For each ground range, the model interpolates the receiver elevation angle using the receiver elevation angles corresponding to the oblique frequencies with the actual operating frequency as the index.
## Interpolation of Virtual Height based on Operating Frequency
The virtual height corresponding to each receiver path length and elevation angle is determined using the same interpolation process. For each ground range, the model interpolates the virtual height using the virtual heights corresponding to the oblique frequencies with the actual operating frequency as the index.
## Calculation of Total Phase
To perform its calculations, the model uses the total phase of an extracted track point. Total phase is calculated from the steer phase of the antenna configuration, the measured phase value of the extracted track point, and the operator-selected Azimuth Repetition Interval (ARI) number.
The ROP Parameters class calculates steer phase by determining the total phase length for the center of the receiver antenna boresight. The receiver boresight is corrected for the mechanical boresight, the current steer, antenna tilt, elevation angle, baseline separation, and delay bias. Then, the ROP Parameters class converts the total phase length to steer phase by dividing by the wavelength.

Figure F‑7. Antenna Geometry

(
0)
(
0)
   (
0)
where:
tilt	Antenna Tilt (Lateral)
steer	Electrical Steer plus Flex Steer
phi	Receive Elevation Angle (design parameter for fixed, controlled for Flex)
baseline	Separation distance between Antenna Phase Centers
delaybias	Distance of Bias Cabling
steerphase	Total Phase at steered Azimuth and Elevation
c	Speed of light
	Operating Wavelength
FOP	Operating Frequency
totalphaselength	The distance assoicated with the phase difference between phase centers

The track extraction software calculates the total phase of each extracted point using the steer phase, the phase value of the extracted track point, and the operator selected ARI.
Antenna tilt is defined as follows: From behind the array, looking in the direction of the array boresight; if the left hand side of the array is lower than the right hand side, the tilt is positive.
  (19a)
where:
TotalPhase	Total Phase of incoming signal
phasevalue	Phase value of the extracted track point
steerphase	Steer Phase
n	ARI number (0 = center)

## Calculation of Azimuth for Total Phase value
The model uses the total phase value to calculate the target azimuth for each receiver elevation angle. The azimuth is corrected for the mechanical boresight, antenna tilt, baseline, and delay bias.
(
0)
where:
Azimuth	Target Azimuth
Boresight	Mechanical Boresight of the Antenna
tilt	Antenna Tilt (Lateral)
rx_elev	Receive Elevation Angle (design for fixed, steered for flex)
baseline	Distance between Antenna Phase Centers
delaybias	Distance of Bias Cabling
totalphase	Total Phase of incoming signal
c	Speed of light
FOP	Operating Frequency

Geo-positioning a target introduces an azimuth offset into the output of the ionospheric model in addition to the range-dependant vertical height terms discussed in Section F.8. The azimuth effect of geo-positioning is treated as an offset that is applied to all tracks sharing the same propagation layer. Geo-positioning events at different times within an ADS result in a time sequence of azimuth offsets which are interpolated to provide a single offset that is applied to the azimuth calculated in the equation above.
## Calculation of Transmitter Ground Range
The model then determines the transmitter ground range by using the spherical geometry of the earth combined with a given azimuth and receiver ground range. The distance and bearing between the receiver and the transmitter are known. Each combination of receiver ground range and target azimuth will produce a spherical triangle with the receiver, transmitter and target.

(
0)
(
0)
where:
RE	Radius of Earth (sea level)
GRTX	Ground Range from Transmitter
GRRX	Ground Range from Receiver
DTXRX	Distance between Transmitter and Receiver
ATXRX	Bearing from Transmitter to Receiver
	Angle between the target and the transmitter measured at the receiver
Az	Azimuth

The result is a table that contains the Tx Ground Range which corresponds to each assumed Rx Ground Range.
Table F‑6
GRRX #1	GRRX #2	GRRX #3	GRRX #4
Tx Ground Range #1	Tx Ground Range #2	Tx Ground Range #3	Tx Ground Range #4

## Interpolation of Transmitter Path Length using Transmitter Ground Range
The model uses the relationship between receiver ground range and receiver path length to interpolate the transmitter path length associated with each transmitter ground range.
The result is a table that contains the Tx Path Length that corresponds to each assumed Rx Ground Range.
Table F‑7
GRRX #1	GRRX #2	GRRX #3	GRRX #4
Tx Path Length #1	Tx Path Length #2	Tx Path Length #3	Tx Path Length #4

## Interpolation of Transmitter Elevation Angle using Transmitter Ground Range
The model uses the relationship between receiver ground range and receiver elevation angle to interpolate the transmitter elevation angle associated with each transmitter ground range.
The result is a table that contains the Tx Elevation Angle that corresponds to each assumed Rx Ground Range.
Table F‑8
GRRX #1	GRRX #2	GRRX #3	GRRX #4
Tx Elevation Angle #1	Tx Elevation Angle #2	Tx Elevation Angle #3	Tx Elevation Angle #4

## Determination of Radar Range using the two Path Lengths
The model determines the radar range from the site to the target by adding the receiver path length and the transmitter path length. Then, it subtracts the distance between the transmitter and receiver and dividing by two. The resulting distance is the average radar range to the target. This calculation is done for each receiver ground range.
(0)
where:
PathTX	Path Length from Transmitter
PathRX	Path Length from Receiver
RR	Radar Range
DTXRX	Distance between Transmitter and Receiver

Table F‑9
	GRRX #1	GRRX #2	GRRX #3	GRRX #4
Path_RX	PathRX	PathRX	PathRX	PathRX
Path_TX	PathTX	PathTX	PathTX	PathTX
Radar_Range	RR	RR	RR	RR

## Interpolation of Receiver Ground Range using Measured Radar Range
The model calculates receiver ground range using the measured value for radar range. The model does this by interpolation using the relationship between radar ranges and receiver ground ranges.
## Interpolation of Azimuth using Measured Radar Range
The model calculates target azimuth using the measured value for radar range. The model does this by interpolation using the relationship between radar ranges and target azimuths.
## Interpolation of other parameters using Radar Range
The model calculates transmitter path length using the measured value for radar range. The model does this by interpolation using the relationship between radar ranges and transmitter path lengths.
The model calculates transmitter elevation angle using the measured value for radar range. The model does this by interpolation using the relationship between radar ranges and transmitter elevation angles.
The model calculates transmitter ground range using the measured value for radar range. The model does this by interpolation using the relationship between radar ranges and transmitter ground ranges.
The model calculates receiver path length using the previously calculated value for receiver ground range. The model does this by interpolation using the relationship between receiver ground ranges and receiver path lengths.
The model calculates receiver elevation angle using the previously calculated value for receiver ground range. The model does this by interpolation using the relationship between receiver ground ranges and receiver elevation angles.
The model calculates virtual height using the previously calculated value for receiver ground range. The model does this by interpolation using the relationship between receiver ground ranges and virtual heights.
## Calculation of Other Parameters
Since the model assumes the propagation path can be modeled by a triangle, the model sets the target ray receive angle to be the same the transmitter elevation angle. The model also sets the target ray reflect angle to be the same as the receiver elevation angle.
## Calculation of Alternate Target Azimuth and Receiver Ground Range
The model also calculates the target azimuth and receiver ground range to an alternate target location. If the calculated target azimuth is to the right of the antenna boresight, the alternate target location is one ARI to the left. If the calculated target azimuth is to the left of the antenna boresight, the alternate target location is one ARI to the right.
To calculate the alternate location data, the model adds or subtracts 2 (which corresponds to one ARI) to the measured total phase and then recalculates target azimuth and receiver ground range.
## Calculation of LAT/LONG from Receiver Ground Range and Azimuth
Calculation of ground track latitude and longitude is done after the receiver ground ranges and target azimuths have been calculated for every extracted track point within a ground track. The calculation is done outside of the model by the xtv_get_derived_data_class. A track point’s latitude and longitude is calculated using the track point’s receiver ground range (as calculated by the model) and smoothed azimuth. Smoothed azimuth is simply the average of all of the track point target azimuths within a operator specified time window around the track point.
The latitude and longitude calculations are performed by freeware Fortran subroutines that use the WGS84 ellipsoid earth model.
## Reference Tables
Table F‑10. Variables and Constants
GRTX	Ground Range from Transmitter
GRRX	Ground Range from Receiver
PathTX	Path Length from Transmitter
PathRX	Path Length from Receiver
RR	Radar Range
VIH	Vertical Height (a function of ground range if a target has been geo-positioned)
VIF	Vertical Frequency
RE	Radius of Earth (sea level)
DTXRX	Distance between Transmitter and Receiver
ATXRX	Bearing from Transmitter to Receiver
	Angle between the target and the transmitter measured at the receiver
Az	Azimuth
FOP	Operating Frequency
tilt	Antenna Tilt (Lateral)
steer	Electrical Steer (including flex)
phi	Antenna Elevation (design parameter for fixed antennas, controlled value for flex)
baseline	Distance between Antenna Phase Centers
delaybias	Distance of Bias Cabling
totalphase	Total Phase of incoming signal
totalphaselength	The distance associated with the phase difference between phase centers at the current steer and elevation angle.
c	Speed of Light
	Operating Wavelength
OIK	Olbique Correction Factor
OIF	Oblique Frequency
k	Smith Factor
I	Angle of Incidence
QVIF	Quasi-vertical frequency
QVIH	Quasi-vertical height

Table F‑11. Propagation Triangle
X	The segment that connects the receiver and intersects the side from the the center of the Earth to the reflection point perpendicularly
Y	The segment from the reflection point to the intersection with segment X
Y’	The Segment from the center of the Earth to the intersection with segment X
	Angle at the receiver
	Elevation Angle at Receiver less the right angle for the intersection with the Surface of the Earth.